GliGli’s Overcycler
Affordable polyphonic hybrid single cycle / analog synthesizer.

# Introduction
This project started about 10 years ago, when I wanted to make use of spare SSM2044 voltage controlled low pass filters I had lying around.
It went through 3 major revisions until it became the full-fledged retail synthesizer it is now.
There is 2 versions of this synthesizer, “Fully built” and “DIY”. This manual is about operating the synthesizer for both. Build instructions for the “DIY” version will be available in another document.
# Overview
## Features
- 6 voice polyphony using hybrid synthesis (Digital "single cycle" oscillators / per-voice analog voltage-controlled filter and voltage-controlled amplifier).
- 2 synchronizable oscillators per voice, duty cycle modulation on any waveform, dual waveform mix modulation, "grith" modulation (from a subtle veil to "ring modulation"-like sounds), 64KHz sample rate for a clean sound by default.
- 3 complete envelopes with linear/exponential choice and looping (oscillators / filter / amplifier).
- 2 complete low frequency oscillators with 6 modulation destinations.
- 1 noise generator.
- Voice panning on the stereo output.
- Sequencer / Arpeggiator.
- Patches and single cycles (AKWF, ProphetVS,...) stored on an internal flash chip, accessible through USB mass storage.
- USB powered with USB MIDI and regular MIDI, CCs for coarse values, NRPN, channel after-touch,...
## Front panel




 Back-lit character LCD screen, 4 rows of 40 characters.
 10 potentiometers, in 2 rows of 5.
 Keypad, 4 rows of 4 keys.
## Rear panel

 Main output 6,35mm jacks.






- Connect a single jack to get TRS (tip-ring-sleeve) stereo (eg. headphones).
- Connect 2 jacks to get TS (tip-sleeve) left and right stereo (eg. connect to 2 mono channels on a mixer).
Note: As synthesizer voices are hard-panned on the stereo output, it is recommended to connect to a mixer through 2 mono channels, that way mixer channel panning can be used to moderate the stereo effect (by setting channel panning symmetrically from the center).
 Main volume knob, from low volume (left) to high volume (right).
 DIN MIDI input.
 Pedal (aka. foot switch) TS input jack, “press to connect” configuration.
- Acts as a sustain input when not arpeggiating or in unison mode.
- Holds the arpeggiator pattern when arpeggiating (has priority over sustain).
- Sets a chord pattern when in unison mode (has priority over sustain and arpeggiator hold).
 USB-B input, power input for the synthesizer and can used for USB MIDI and for internal disk access through USB mass storage.
 On / off switch, pressed is on.
## Basic ergonomics
# The pages
## Oscillators
## WaveMod
## Filter
## Amplifier
## LFO 1
## LFO 2
## Arpeggiator
## Sequencer
## Miscellaneous
## Presets
# Maintenance
## Adding single-cycle waveforms
## Data backup
## Upgrading the firmware
# MIDI implementation
## Chart
## Detailed continuous controllers
## NRPN parameters list