GliGli’s Overcycler
Affordable polyphonic hybrid single cycle / analog synthesizer.

# Introduction

This project started about 10 years ago, when I wanted to make use of spare SSM2044 voltage controlled low pass filters I had lying around.
It went through 3 major revisions until it became the full-fledged retail synthesizer it is now.
There is 2 versions of this synthesizer, “Fully built” and “DIY”. This manual is about operating the synthesizer for both. Build instructions for the “DIY” version will be available in another document.
# Overview
## Features
- 6 voice polyphony using hybrid synthesis (Digital "single cycle" oscillators / per-voice analog voltage-controlled filter and voltage-controlled amplifier).
- 2 synchronizable oscillators per voice, duty cycle modulation on any waveform, dual waveform mix modulation, "grith" modulation (from a subtle veil to "ring modulation"-like sounds), 64KHz sample rate for a clean sound by default.
- 3 complete envelopes with linear/exponential choice and looping (oscillators / filter / amplifier).
- 2 complete low frequency oscillators with 6 modulation destinations.
- 1 noise generator.
- Voice panning on the stereo output.
- Sequencer / Arpeggiator.
- Patches and single cycles (AKWF, ProphetVS,...) stored on an internal flash chip, accessible through USB mass storage.
- USB powered with USB MIDI and regular MIDI, CCs for coarse values, NRPN, channel after-touch,...
## Front panel




 Back-lit character LCD screen, 4 rows of 40 characters.
 10 potentiometers, in 2 rows of 5.
 Keypad, 4 rows of 4 keys.
## Rear panel

 Main output 6,35mm jacks.






- Connect a single jack to get TRS (tip-ring-sleeve) stereo (eg. headphones).
- Connect 2 jacks to get TS (tip-sleeve) left and right stereo (eg. connect to 2 mono channels on a mixer).
Note: As synthesizer voices are hard-panned on the stereo output, it is recommended to connect to a mixer through 2 mono channels, that way mixer channel panning can be used to moderate the stereo effect (by setting channel panning symmetrically from the center).
 Main volume knob, from low volume (left) to high volume (right).
 DIN MIDI input.
 Pedal (aka. foot switch) 6,35mm TS input jack, “press to connect” configuration.
- Acts as a sustain input when not arpeggiating or in unison mode.
- Holds the arpeggiator pattern when arpeggiating (has priority over sustain).
- Sets a chord pattern when in unison mode (has priority over sustain and arpeggiator hold).
 USB-B input, power input for the synthesizer. It can also be used for USB MIDI and for internal disk access through USB mass storage.
 Synthesizer on / off switch, pressed is on.
## Basic ergonomics

Basically, ergonomics are centered around the use of the screen, mainly to show potentiometers and buttons values for the current page of parameters.
### The main screen






 2 rows of 5 parameters, one for each potentiometer from the front panel. Each parameter has a short name on 4 characters and a value. Turning a potentiometer will allow changing the corresponding parameter value through the “Potentiometer edit screen”.
 4 rows of parameters, corresponding to the rightmost A / B / C / D buttons of the keypad. Pressing one of those keypad keys will allow changing the corresponding parameter to a new value through the “Button edit screen”.
 ”Preset modified” indicator. Changing any parameter from the current preset will show this indicator as a remainder that changes many need to be saved to persist.
 .”Voice activity” indicators. One for each of the 6 voices, giving an overview of the amplifier envelope state for each voice. The layout is as follows:
Voice 1	Voice 2
Voice 3	Voice 4
Voice 5	Voice 6

### The potentiometer edit screen

When a potentiometer is turned, this screen shows detailed information about the parameter being edited:
- The parameter long name at the top.
- The current parameter value in the middle.
- A bar-graph showing the approximate value at a glance.
When the current potentiometer position is out of range, and the value hasn’t been reacquired (that is, the potentiometer is still locked to its previous value), the screen will show one of two arrows around the numerical value to hint which way it should be turned.
Note: when more than one potentiometer is turned at the same time, this screen will not show. Instead, the main screen will directly reflect the changes.

### The button edit screen

When a button (A / B /C / D) is pressed, this screen shows detailed information about the parameter being edited:
- The parameter long name at the top.
- The current parameter value in the middle.
- A list of all the possible values for the parameter, with an arrow indicating which is currently chosen.
Note: some buttons are used for actions, in that case the action is performed as soon as the button is pressed and this screen only shows the action long name.
# The pages
## Oscillators
## WaveMod
## Filter
## Amplifier
## LFO 1
## LFO 2
## Arpeggiator
## Sequencer
## Miscellaneous
## Presets
# Maintenance
## Adding single-cycle waveforms
## Data backup
## Upgrading the firmware
# MIDI implementation
## Chart
## Detailed continuous controllers
## NRPN parameters list